All-New Ford Transit – Preliminary Technical Specifications

Range Overview

| All-New Transit Van |
| --- |
|  | L1 | L2 | L3 | L4 | L5 |
| Wheelbase (mm) |  | 3300 | 3750 | 3750 |  |
| Overall length (mm) |  | 5531 | 5981 | 6704 |  |
| GVM range (kg) |  | 2900 to 3500 | 3100 to 3700 | 3500 to 4700 |  |
| Roof options (overall unladen height, mm) |  | 2550 (H2) 2789 (H3) | 2547 (H2) 2786 (H3) | 2781 (H3) |  |
| Driveline options (for GVM range, kg) |  | FWD (2900 to 3500) RWD (3500) AWD (3500) | FWD (3100 to 3500) RWD (3500 to 3700) AWD (3500) | RWD (3500 to 4700) AWD (3500) |  |
| Available bodystyles | Van, Double-cab-in-van, Kombi, Kombi van (availability varies according to length, GVM and driveline) |

| All-New Transit M2 Bus |
| --- |
|  | L1 | L2 | L3 | L4 | L5 |
| Wheelbase (mm) |  | 3300 | 3750 | 3750 |  |
| Overall length (mm) |  | 5531 | 5981 | 6704 |  |
| Seating capacity |  | 11/12 seats | 14/15 seats | 17/18 seats |  |
| GVM range (kg) |  | 3500 to 3750 | 4100 | 4600 |  |
| Roof options (overall unladen height, mm) |  | 2550 (H2) 2789 (H3) | 2547 (H2) 2786 (H3) | 2781 (H3) |  |
| Driveline options |  | RWD | RWD | RWD |  |

| All-New Transit Chassis Cab |
| --- |
|  | L1 | L2 | L3 | L4 | L5 |
| Wheelbase (mm) | 3137 | 3504 | 3954 | 3954 | 4522 |
| Overall length (mm) (Single/Double Cab) | 5205 | 5572 | 6022 | 6579/6404 | 7577/7394 |
| Chassis frame length* (mm) (Single/Double Cab) | 2775 | 3142/2327 | 3592/2777 | 4149/3159 | 5147/4149 |
| GVM range (kg) | 3100 to 3300 | 3100 to 4700 | 3500 to 4700 | 3500 to 4700 | 3500 to 4700 |
| Overall unladen cab height (mm) (Single/Double Cab) | 2219 | 2214/2205 | 2207/2199 | 2207/2200 | 2197/2191 |
| Driveline options (for GVM range, kg) | RWD (3100 to 3300) AWD (3300) | FWD (3100 to 3500) RWD (3500 to 4700) AWD (3500) | FWD (3500) RWD (3500 to 4700) AWD (3500) | FWD (3500) RWD (3500 to 4700) AWD (3500) | RWD (3500 to 4700) AWD (3500) |
| Available variants | Single chassis cab, Double chassis cab, Chassis cowl, Skeletal chassis (availability varies according to length, GVM and driveline) |

* Including light bar

Ford will be introducing the full new Transit range using a staggered approach, with a second phase including the DCiV, Kombi, Kombi Van, Chassis Cab L5 and Double Chassis Cab variants available from the final quarter of 2014.

Sample vehicle specifications

Ford Transit 350 ECOnetic Medium Wheelbase/Medium Roof (L2/H2) – Preliminary Specs†

| Engine data |
| --- |
| Engine type | Duratorq TDCi 2.2-litre (ECOnetic) |
| Displacement – cc | 2198 |
| Fuel type | Diesel |
| Bore mm | 86.0 |
| Stroke mm | 94.6 |
| Max power PS (kW) at rpm | 125 (92) at 3500 |
| Max Torque in Nm at rpm | 350 at 1450—2000 |
| Driveline |
| Configuration | Front-wheel drive, transverse engine. Standard Auto-Start-Stop Fitted with optional fixed 100km/h (62mph) speed limiter |
| Transmission | VMT6 six-speed manual transmission (Final drive 4.19) |
| Performance |
| Fuel Economy * Litres/100km | urban | extra urban | combined |
|  | 7.3 | 5.9 | 6.4 |
| CO2 g/km (average) | 169 |
| Construction |
| Front Suspension | Independent MacPherson struts, variable rate coil springs, stabiliser bar and gas pressurised shock absorbers |
| Rear Suspension | Leaf springs, gas pressurised shock absorbers |
| Brakes | Dual-circuit, with servo-assistance. Front and rear discs. Standard Electronic Stability Control (ESC) |
| Steering | Rack and pinion, power assisted, adjustable in reach and rake |
| Weights and dimension |
| Base kerb weight (kg)** | 1972 |
| Payload (kg)** | 1453 |
| GVM (kg) | 3500 |
| GTM (kg) | 4250 |
| Braked trailer (kg) | 2000 |
| Unbraked trailer (kg) | 750 |
| Max Roof load (kg) | 100 |
| Wheelbase (mm) | 3300 |
| Max Load Length (mm) | 3083 |
| Max Load Width (mm) | 1784 |
| Load Height (mm) | 1886 |
| Load Volume (m3) | 10.0 (with full bulkhead) |
| Vehicle Length (mm) | 5531 |
| Vehicle Height (mm) | 2542 (unladen) |
| Vehicle Width (mm) with/without mirrors | 2474 / 2059 |

Ford Transit 350 ‘Jumbo’ Long Wheelbase/High Roof (L4/H3) – Preliminary Specs†

| Engine data |
| --- |
| Engine type | Duratorq TDCi 2.2-litre |
| Displacement – cc | 2198 |
| Fuel type | Diesel |
| Bore mm | 86.0 |
| Stroke mm | 94.6 |
| Max power PS (kW) at rpm | 100 (74) at 3500 | 125 (92) at 3500 | 155 (114) at 3500 |
| Max Torque in Nm at rpm | 310 at 1300—2100 | 350 at 1450—2000 | 385 at 1600—2300 |
| Driveline |
| Configuration | Rear-wheel drive, longitudinal engine Fitted with optional Auto-Start-Stop |
| Transmission | MT82 six-speed manual (Final drive 3.31 (100PS) 3.15 (125PS/155PS) |
| Performance |
| Fuel Economy * Litres/100km | urban | extra urban | combined |
|  | 8.9 (100PS) 8.6 (125PS/155PS) | 7.4 (100PS) 7.3 (125PS/155PS) | 8.0 (100PS) 7.8 (125PS/155PS) |
| CO2 g/km (average) | 210 (100PS), 204 (125PS/155PS) |
| Construction |
| Front Suspension | Independent MacPherson struts, variable rate coil springs, stabiliser bar and gas pressurised shock absorbers |
| Rear Suspension | Leaf springs, gas pressurised shock absorbers |
| Brakes | Dual-circuit, with servo-assistance. Front and rear discs. Standard Electronic Stability Control (ESC) |
| Steering | Rack and pinion, power assisted, adjustable in reach and rake |
| Weights and dimension |
| Base kerb weight (kg)** | 2312 |
| Payload (kg)** | 1113 |
| GVM (kg) | 3500 |
| GTM (kg) | 5000 (100PS), 5500 (125PS/155PS) |
| Braked trailer (kg) | 2450 (100PS), 2800 (125PS/155PS) |
| Unbraked trailer (kg) | 750 |
| Max Roof load | 100 |
| Wheelbase (mm) | 3750 |
| Max Load Length (mm) | 4256 |
| Max Load Width (mm) | 1784 |
| Load Height (mm) | 2025 |
| Load Volume (m3) | 15.1 (with full bulkhead) |
| Vehicle Length (mm) | 6704 |
| Vehicle Height (mm) | 2760 (unladen) |
| Vehicle Width (mm) with/without mirrors | 2474 / 2059 |

Notes:

†  The weight, fuel economy and CO2 emissions data quoted here relate to standard UK base specification vehicles. For vehicles sold in other markets, or with optional equipment, this data may vary.

*: The stated fuel consumption and CO2 emissions are measured according to the technical requirements and specifications of the European Regulation (EC) 715/2007 as last amended. Results in MPG also correspond to this European drive cycle and are stated in imperial gallons. The results may differ from fuel economy figures in other regions of the world due to the different drive cycles and regulations used in those markets.

**:Weight  figures refer to base equipment level vehicles in running order including driver (75 kg).

Appendix: Power-/torque curves

2.2-litre Ford Duratorq TDCi 100 PS (Euro Stage 5)

2.2-litre Ford Duratorq TDCi 125 PS (Euro Stage 5)

2.2-litre Ford Duratorq TDCi 155 PS (Euro Stage 5)

Note: The data information in this press release reflects preliminary specifications and was correct at the time of going to print. However, Ford policy is one of continuous product improvement. The right is reserved to change these details at any time.

About Ford Motor Company
Ford Motor Company, a global automotive industry leader based in Dearborn, Mich., manufactures or distributes automobiles across six continents. With about 180,000 employees and 65 plants worldwide, the company’s automotive brands include Ford and Lincoln. The company provides financial services through Ford Motor Credit Company. For more information about Ford and its products worldwide please visit  www.corporate.ford.com.

Ford of Europe is responsible for producing, selling and servicing Ford brand vehicles in 50 individual markets and employs approximately 47,000 employees at its wholly owned facilities and approximately 67,000 people when joint ventures and unconsolidated businesses are included. In addition to Ford Motor Credit Company, Ford Europe operations include Ford Customer Service Division and 22 manufacturing facilities (13 wholly owned or consolidated joint venture facilities and nine unconsolidated joint venture facilities). The first Ford cars were shipped to Europe in 1903 – the same year Ford Motor Company was founded. European production started in 1911.

Contact: Detlef Jenter Ford of Europe +49 221 901 8745 djenter@ford.com